## Slide 1
DESIGN & VERIFICATION OF A
32-Bit Direct-Mapped Cache Controller
L1 Subsystem Implementation with Write-Back Policy & MATLAB Golden Reference Validation
Omar Fawzy Mahmoud | Hatem Mustafa
September 2026

## Slide 2
Introduction & Motivation
The Memory Wall Problem
Processor speeds scale much faster than DRAM access speeds, causing CPU pipeline stalls during memory fetches.
Solution — Cache Memory
A small, ultra-fast SRAM buffer located close to the core, operating at CPU speed.
Core Principles — Locality of Reference
Temporal Locality
Data accessed recently is likely to be accessed again soon.
Spatial Locality
Data adjacent to recently accessed addresses is likely to be accessed soon.
Objective: Reduce Average Memory Access Time (AMAT) and system power consumption.
32-Bit Direct-Mapped Cache Controller
2

## Slide 3
System Specifications & Memory Organization
Architecture: 32-bit CPU interface, 128-bit (16-byte) backing main memory line. Write Policy: Write-Back with Write-Allocate on Write Misses.
32-Bit Address Partitioning
Tag
[31:10]
Index
[9:4]
Word Off.
[3:2]
Byte Off.
[1:0]
22 bits — identifies unique block in memory
6 bits — maps to 2^6 = 64 cache lines
2 bits — selects W0–W3
2 bits — always 2'b00
SRAM Storage Sizing
1 KB
Data Array
64 × 128 bits = 1024 Bytes
1408 b
Tag Array
64 × 22 bits
128 b
Status Flags
64 Valid + 64 Dirty bits
1.216 KB
Total Size
9728 bits
32-Bit Direct-Mapped Cache Controller
3

## Slide 4
Subsystem Architecture
Five cooperating Verilog modules form the L1 cache subsystem.
cache_controller.v
Central FSM managing request latching, line fills, and writebacks.
cache_storage.v
Houses SRAM arrays (Data, Tag, Valid, Dirty) and hit look-up logic.
main_memory.v
Simulates 1024 × 128-bit backing store with single-cycle ready acknowledgment.
perf_counters.v
Tracks total accesses, hits, and misses.
trace_generator.v
Issues automated, repeatable test patterns.
32-Bit Direct-Mapped Cache Controller
4

## Slide 5
Finite State Machine (FSM) Design
3'b000
IDLE
Latches incoming cpu_addr, cpu_wr_data, and flags.
3'b001
COMPARE
Evaluates tag match and valid bit to route hit vs. miss.
3'b010
HIT
Asserts cpu_ready=1, merges 32-bit word on write, returns to IDLE.
3'b011
MISS_WRITEBACK
Flushes modified line: mem_addr = {tag_out, index, 4'b0000}.
3'b100
MISS_WAIT
Issues read request to main memory and waits for mem_ready.
3'b101
FILL
Writes fetched 128-bit block to SRAM, sets valid=1, dirty=0.
Flow: IDLE → COMPARE → (Hit) HIT | (Miss & Dirty) MISS_WRITEBACK → MISS_WAIT → FILL | (Miss & Clean) MISS_WAIT → FILL
32-Bit Direct-Mapped Cache Controller
5

## Slide 6
FSM State Diagram
Full transition diagram for the six-state cache controller.
32-Bit Direct-Mapped Cache Controller
6

## Slide 7
Hardware Debugging & Key Fixes
Bug #1 — Tag Bit-Slice Regression
SYMPTOM
Eviction for 0x00000100 wrote back to incorrect memory address 0x00040100.
ROOT CAUSE
Address generator sliced lower address bits [21:0] instead of upper bits [31:10].
FIX
Updated all state logic in cache_controller.v to slice upper tag bits addr_reg[31:10].
Bug #2 — Late Hit Sampling Synchronization
SYMPTOM
Performance counters recorded false hits during line refills.
ROOT CAUSE
Hit status was sampled in HIT state after FILL had already written valid data.
FIX
Latched was_hit inside the testbench during the COMPARE state.
32-Bit Direct-Mapped Cache Controller
7

## Slide 8
Verification Results: MATLAB vs. Verilog
Metric | MATLAB Golden Model | Verilog Simulation | Alignment
Total Memory Accesses | 38 | 38 | 100% Match
Total Cache Hits | 19 | 19 | 100% Match
Total Cache Misses | 19 | 19 | 100% Match
Dirty Line Evictions | 7 | 7 | 100% Match
Overall Hit Rate | 50.0% | 50.0% | Perfect Alignment
100%
Correlation across every transaction
7 / 7
Dirty evictions to correct block addresses
Verification Insights
100% Correlation — every memory transaction exhibited identical outcomes across both models.
Correct Address Reconstruction — all 7 dirty evictions targeted calculated block addresses accurately.
Data Integrity — word-merging on write hits modified only the targeted 32-bit word, leaving adjacent words intact.
32-Bit Direct-Mapped Cache Controller
8

## Slide 9
Conclusion & Future Work
Summary of Achievements
Successfully designed, implemented, and verified a 32-bit direct-mapped cache subsystem.
6-state FSM controller fully integrated with SRAM and real-time performance tracking.
100% architectural correlation verified against MATLAB golden reference.
Future Work
Extend design to Set-Associative Cache structures (2-way / 4-way).
Implement configurable line-replacement algorithms (e.g., LRU / Pseudo-LRU).
Thank you
32-Bit Direct-Mapped Cache Controller
9